## Slide 1: Arduino Course
Prepared by: Qossay Abu Rida

## Slide 2: Agenda
Embedded system
ADC & DAC
Arduino environment
Basic electronic component
Interrupts
Sensors
Actuators
Communication

## Slide 3: Embedded System

## Slide 4: What is an Embedded System?
Definition: An embedded system is a specialized computer system that is designed to perform a specific task. Unlike general-purpose computers, which can run a variety of applications, embedded systems are dedicated to one or a few functions.
Common Use: Embedded systems are found in many everyday devices, from household appliances to automobiles, medical equipment, and industrial machines.

## Slide 5: Basic Structure of an Embedded System
1- Microcontroller/Microprocessor:
  The brain of the embedded system.
  Executes programmed instructions to perform specific tasks.
  Example: Arduino uses the ATmega328 microcontroller.
2- Memory:
  RAM (Random Access Memory): Temporary storage for data and instructions currently in use.
  ROM (Read-Only Memory): Permanent storage for the system's firmware and operating instructions.

## Slide 6
3- Input Devices:
  Collect data from the external environment.
  Examples: Sensors, buttons, keyboards.
4- Output Devices:
  Deliver data or actions to the external environment.
  Examples: Displays, LEDs, motors.
5- Power Supply:
  Provides the necessary power for the system to operate.
  Can be battery-operated or connected to a power source.
6- Communication Interfaces:
  Allow the system to communicate with other systems or devices.
  Examples: Serial ports, USB, Wi-Fi, Bluetooth.

## Slide 7: Basic Structure (Symbolic-Based)

## Slide 8: Example of an Embedded System: Digital Thermometer
Microcontroller: Reads temperature data from the sensor and processes it.
Sensor: Measures the temperature and sends data to the microcontroller.
Display: Shows the temperature reading to the user.
Buttons: Allow users to switch between Celsius and Fahrenheit or reset the device.
Power Supply: Battery that powers the thermometer.

## Slide 9: ADC & DAC

## Slide 10
What is an ADC?
Definition: An Analog-to-Digital Converter (ADC) is a device that converts analog signals (continuous signals) into digital signals (discrete signals) that a microcontroller or computer can process.
Purpose: To allow digital systems to interact with the real world by converting analog inputs (e.g., temperature, sound, light) into a format they can understand and process.
What is a DAC?
Definition: A Digital-to-Analog Converter (DAC) is a device that converts digital signals (discrete signals) into analog signals (continuous signals).
Purpose: To allow digital systems to produce analog outputs (e.g., audio signals, light intensity control) that can be used in the real world.

## Slide 11
How ADC Works
  Sampling: The analog signal is sampled at regular intervals.
  Quantization: Each sample is approximated to the nearest value within a range.
  Encoding: The quantized values are converted into binary code.

## Slide 12
How DAC Works
  Input: The digital signal is received from a microcontroller or computer.
  Conversion: The digital values are converted to corresponding analog values.
  Output: The analog signal is output to drive an analog device.

## Slide 13: Arduino Environment

## Slide 14: Arduino Hardware
Arduino Boards
  Microcontroller-based boards with various input/output capabilities.
  Examples: Arduino Uno, Arduino Mega, Arduino Nano.
Key Components
  Microcontroller: The brain of the board (e.g., ATmega328 on Arduino Uno).
  Digital Pins: Used for digital input/output (e.g., LEDs, buttons).
  Analog Pins: Used for analog input (e.g., sensors).
  Power Supply: Can be powered via USB or external power source.
  Communication Ports: Serial, I2C, SPI for interfacing with other devices.

## Slide 15
Arduino Uno board with labeled components.

## Slide 16: Arduino Software (Arduino IDE)
Arduino IDE
  Integrated Development Environment for writing, compiling, and uploading code to Arduino boards.
  Available for Windows, Mac, and Linux.
Key Features
  Code Editor: Write and edit Arduino sketches (programs).
  Compiler: Convert sketches into machine code that the microcontroller can execute.
  Uploader: Transfer the compiled code to the Arduino board via USB.
  Serial Monitor: Communicate with the board and debug sketches using serial communication.
Programming Language
  Based on C/C++ with simplified syntax and functions.
  Uses libraries to add functionality (e.g., controlling motors, reading sensors).

## Slide 17
Arduino IDE simple sketch.

## Slide 18: How to Download the Arduino IDE ?
Visit the Arduino Website:
Open your web browser and go to arduino.cc
Navigate to the Software Section:
Hover over "Software" in the main menu.
Click on "Downloads."
Choose Your Operating System:
Select the version for your OS (Windows, Mac, Linux).
Download the Installer:
Click "Just Download" if prompted for a donation.

## Slide 19: How to Program Arduino and Code Structure
Setup Function:
  Purpose: Initializes settings.
  Runs Once: This code runs once when the Arduino is powered on or reset.
Loop Function:
  Purpose: Contains the main logic of the program.
  Runs Repeatedly: This code runs in a loop after the setup function has completed.

## Slide 20: Common Functions Used in Arduino Programming
pinMode():
  Purpose: Configures a specified pin to behave either as an input or an output.
digitalWrite():
  Purpose: Sets a specified digital pin to HIGH or LOW.
digitalRead():
  Purpose: Reads the value from a specified digital pin, either HIGH or LOW.

## Slide 21: Common Functions Used in Arduino Programming
analogRead():
  Purpose: Reads the value from a specified analog pin.
analogWrite():
  Purpose: Writes an analog value (PWM wave) to a specified pin.

## Slide 22: Common Functions Used in Arduino Programming
delay():
  Purpose: Pauses the program for a specified number of milliseconds.
millis():
  Purpose: Returns the number of milliseconds since the Arduino board began running the current program.

## Slide 23: Common Functions Used in Arduino Programming
Serial.begin():
  Purpose: Sets the data rate in bits per second (baud) for serial data transmission.
Serial.print():
  Purpose: Prints data to the serial port as human-readable ASCII text.
Serial.println():
  Purpose: Prints data to the serial port as human-readable ASCII text, followed by a carriage return character.

## Slide 24: Example 1 => Blinking LED
Blinking LED using Delay function:

## Slide 25: Example 2 => Blinking LED
Blinking LED using millis function:

## Slide 26: Basic Electronic Component

## Slide 27: LED (Light Emitting Diode)
Definition: A semiconductor device that emits light when an electric current passes through it.
Usage: Visual indicators, status lights, displays.
Connection:
    Anode (+): Connected to a positive voltage.
    Cathode (-): Connected to ground, usually through a current-limiting resistor.

## Slide 28: Button
Definition: A simple switch used to make or break a connection in an electric circuit.
Usage: User inputs, control signals, event triggers.
Connection:Typically connected between a digital input pin and ground or VCC.

## Slide 29
Pull-Up and Pull-Down Resistors:
Pull-Up: Connects the pin to VCC (high voltage) through a resistor, ensuring a known state when the button is not pressed.
Pull-Down: Connects the pin to ground (low voltage) through a resistor, ensuring a known state when the button is not pressed.
Internal Pull-Up: Use pinMode(pin, INPUT_PULLUP); to enable the internal pull-up resistor.

## Slide 30: Potentiometer
Definition: A three-terminal resistor with a sliding or rotating contact that forms an adjustable voltage divider.
Usage: Variable resistors, volume controls, sensor calibration.
  Connection:Wiper: Connected to an analog input pin.
  Other Terminals: Connected to VCC and ground

## Slide 31: LED (Light Emitting Diode)
LED (Light Emitting Diode)
Definition: A semiconductor device that emits light when an electric current passes through it.
Usage: Visual indicators, status lights, displays.
Connection:
    Anode (+): Connected to a positive voltage.
    Cathode (-): Connected to ground, usually through a current-limiting resistor.

## Slide 32: Interrupts

## Slide 33: What are Interrupts?
Definition: Interrupts are signals that temporarily halt the main program execution to immediately run a special function called an Interrupt Service Routine (ISR).
Purpose: To handle time-critical tasks, respond to external events, or process real-time signals without delay.
Benefits: Allows for efficient handling of tasks without continuously checking for events within the main loop.

## Slide 34: Using Interrupts in Arduino
Attaching an Interrupt:
  Use the attachInterrupt() function to specify which pin and condition will trigger the interrupt, and which ISR to call.
  Parameters:
    pin: The pin number where the interrupt is attached.
    ISR: The name of the function to call when the interrupt occurs.
    mode: The condition that triggers the interrupt (LOW, CHANGE, RISING, FALLING).

## Slide 35: Example 3 => Toggle LED
Toggle LED without interrupts:

## Slide 36: Example 4 => Toggle LED
Toggle LED with interrupts:

## Slide 37: Example 5 => Toggle LED
Toggle LED with interrupts and avoid bouncing effect:

## Slide 38: Examples for training

## Slide 39: Example 6 => Toggle LED
Toggle LED without interrupts:

## Slide 40: LCD liquid crystal display

## Slide 41: Sensors

## Slide 42: Actuators

## Slide 43: Communication

## Slide 44: Contact us