## Slide 1: Advanced Arduino Course
Prepared by: Qossay Abu Rida
IEEE Robotics and Automation Society

## Slide 2: Introduction

## Slide 3: Embedded systems (Symbolic-Based)

## Slide 4: Arduino Hardware
Arduino Boards
  Microcontroller-based boards with various input/output capabilities.
  Examples: Arduino Uno, Arduino Mega, Arduino Nano.
Key Components
  Microcontroller: The brain of the board (e.g., ATmega328 on Arduino Uno).
  Digital Pins: Used for digital input/output (e.g., LEDs, buttons).
  Analog Pins: Used for analog input (e.g., sensors).
  Power Supply: Can be powered via USB or external power source.
  Communication Ports: Serial, I2C, SPI for interfacing with other devices.

## Slide 5: ESP32 Hardware
ESP32 Overview
  A low-power Wi-Fi and Bluetooth microcontroller with various input/output capabilities.
  Developed by Espressif Systems, commonly used in IoT applications.
Key Components
  Microcontroller: Dual-core Tensilica Xtensa LX6 processor with up to 240 MHz clock speed.
  Digital Pins: Supports multiple GPIO pins for digital input/output operations.
  Analog Pins: Features ADC (Analog-to-Digital Converter) and DAC (Digital-to-Analog Converter).
  Power Supply: Operates at 3.3V, powered via USB or external Li-ion battery.
  Wireless Connectivity: Built-in Wi-Fi (802.11 b/g/n) and Bluetooth (Classic & BLE) for wireless communication.
  Communication Ports: Supports UART, I2C, SPI, PWM, and CAN protocols for external device interfacing.

## Slide 6
Arduino Uno board

## Slide 7
ESP-32 board

## Slide 8: Arduino Software (use for Arduino UNO & ESP32)
Arduino IDE
  Integrated Development Environment for writing, compiling, and uploading code to Arduino boards.
  Available for Windows, Mac, and Linux.
Key Features
  Code Editor: Write and edit Arduino sketches (programs).
  Compiler: Convert sketches into machine code that the microcontroller can execute.
  Uploader: Transfer the compiled code to the Arduino board via USB.
  Serial Monitor: Communicate with the board and debug sketches using serial communication.
Programming Language
  Based on C/C++ with simplified syntax and functions.
  Uses libraries to add functionality (e.g., controlling motors, reading sensors).

## Slide 9: How to Program Arduino & ESP 32
Setup Function:
  Purpose: Initializes settings.
  Runs Once: This code runs once when the Arduino is powered on or reset.
Loop Function:
  Purpose: Contains the main logic of the program.
  Runs Repeatedly: This code runs in a loop after the setup function has completed.

## Slide 10
Arduino IDE simple sketch.

## Slide 11: Common Functions Used in Arduino Programming
pinMode():
  Purpose: Configures a specified pin to behave either as an input or an output.
digitalWrite():
  Purpose: Sets a specified digital pin to HIGH or LOW.
digitalRead():
  Purpose: Reads the value from a specified digital pin, either HIGH or LOW.

## Slide 12: Example:

## Slide 13: Common Functions Used in Arduino Programming
analogRead():
  Purpose: Reads the value from a specified analog pin.
analogWrite():
  Purpose: Writes an analog value (PWM wave) to a specified pin.

## Slide 14: Example:

## Slide 15: Common Functions Used in Arduino Programming
delay():
  Purpose: Pauses the program for a specified number of milliseconds.
millis():
  Purpose: Returns the number of milliseconds since the Arduino board began running the current program.

## Slide 16: Common Functions Used in Arduino Programming
Serial.begin():
  Purpose: Sets the data rate in bits per second (baud) for serial data transmission.
Serial.print():
  Purpose: Prints data to the serial port as human-readable ASCII text.
Serial.println():
  Purpose: Prints data to the serial port as human-readable ASCII text, followed by a carriage return character.

## Slide 17: Interrupts
Definition
  Interrupts are signals that temporarily halt the main program execution to immediately run a special function called an Interrupt Service Routine (ISR).
Purpose
  To handle time-critical tasks, respond to external events, or process real-time signals without delay.
Benefits
  Allows for efficient handling of tasks without continuously checking for events within the main loop.

## Slide 18: Using Interrupts in Arduino
Attaching an Interrupt:
  Use the attachInterrupt() function to specify which pin and condition will trigger the interrupt, and which ISR to call.
  Parameters:
    pin: The pin number where the interrupt is attached.
    ISR: The name of the function to call when the interrupt occurs.
    mode: The condition that triggers the interrupt (LOW, CHANGE, RISING, FALLING).

## Slide 19: Example:

## Slide 20: Sensors

## Slide 21: Ultrasonic Sensor
Introduction:
  Definition: Ultrasonic sensors use sound waves to measure the distance between the sensor and an object.
  Common Model: HC-SR04.
Working Principle:
  Sound Waves: Sends out an ultrasonic wave and measures the time it takes for the echo to return.
  Distance Calculation: Uses the speed of sound to calculate distance based on the time it took for the echo to return.

## Slide 22
Pin Configuration
VCC: +5V Power Supply
GND: Ground
Trig: Trigger Pin
Echo: Echo Pin

## Slide 23: Example:

## Slide 24: IR Sensor
Introduction:
  Definition: Infrared (IR) sensors use infrared light to detect objects or measure the distance between the sensor and an object.
  Common Model: TCRT5000.
Working Principle:
  Infrared Light: Emits an infrared light beam and detects the reflection from an object.
  Distance Calculation: Measures the intensity of the reflected light to determine the presence or distance of an object.

## Slide 25
Pin Configuration
VCC: +5V Power Supply
GND: Ground
OUT: Output pin

## Slide 26
Other models for the IR sensor

## Slide 27: Example:

## Slide 28: LIDAR Sensor
Introduction:
  Definition: The VL6180X is a laser range finder (micro LIDAR) that uses time-of-flight (ToF) technology to measure the distance between the sensor and an object with high precision.
  Common Model: VL6180X.
Working Principle:
  Laser Emission: Emits a laser pulse toward the target object.
  Time-of-Flight Measurement: Measures the time it takes for the laser pulse to reflect off the object and return to the sensor.
  Distance Calculation: Uses the speed of light to calculate the distance based on the time-of-flight of the laser pulse.

## Slide 29
Pin Configuration
VCC: +5V Power Supply
GND: Ground
I2C PIN: Communication with the sensor

## Slide 30: Example:

## Slide 31
Motor

## Slide 32: H-Bridge
Introduction:
  Definition: An H-Bridge is an electronic circuit that enables a voltage to be applied across a load in either direction.
  Common Use: Motor control, allowing motors to run forward or backward.
Working Principle:
  Configuration: Consists of four switches (transistors or MOSFETs) that control the direction of current flow.
  Direction Control: By closing different pairs of switches, the direction of the current and thus the motor's direction can be controlled.

## Slide 33
Pin Configuration
IN1, IN2, IN3, IN4: Input pins to control the switches.
ENA, ENB: Enable pins to activate the H-Bridge channels.
OUT1, OUT2, OUT3, OUT4: Output pins connected to the motor.
VCC: Voltage supply for the H-Bridge.
GND: Ground.12V: Power supply for the motors.

## Slide 34: Examples

## Slide 35: Example 1 => Blinking LED
Blinking LED using Delay function:

## Slide 36: Example 2 => Blinking LED
Blinking LED using millis function:

## Slide 37: Example 3 => Toggle LED
Toggle LED without interrupts:

## Slide 38: Example 4 => Toggle LED
Toggle LED with interrupts:

## Slide 39: Example 5 => Toggle LED
Toggle LED with interrupts and avoid bouncing effect:

## Slide 40: Example 6 => Controlling LED
Creating an interactive system using an Arduino that involves the following components:
Potentiometer
Button
LED
Requirements:
The potentiometer should control the brightness of the LED.
Button should toggle the LED on and off.
Use interrupts to handle the button presses efficiently.

## Slide 41: Example 6 => Controlling LED

## Slide 42: Example 6 => Controlling LED

## Slide 43: Example 7 => Controlling Array of LEDs Unsolved example
You need to create an Arduino system that controls four LEDs based on the value of a potentiometer.
Requirements:Use a potentiometer to determine how many LEDs should be turned on.
The system should work as follows:
If the potentiometer value is between 0 and 255, turn on 1 LED.
If the potentiometer value is between 256 and 511, turn on 2 LEDs.
If the potentiometer value is between 512 and 767, turn on 3 LEDs.
If the potentiometer value is between 768 and 1023, turn on all 4 LEDs.

## Slide 44: Example 8 => LED Reaction Game Unsolved example
Design an Arduino-based reaction game that uses LEDs, a potentiometer, and a button. The goal of the game is to test the player's reaction time.
Requirements:
Use a potentiometer to set the difficulty level of the game.
An LED should light up randomly after a delay.
The player must press a button as quickly as possible when the LED lights up.
The system should display the player's reaction time using LEDs.
The game should reset automatically after displaying the reaction time.

## Slide 45: Example 9 => Print Your Name

## Slide 46: Example 9 => Print Your Name

## Slide 47: Example 10 => Distance Measurement

## Slide 48: Example 10 => Distance Measurement
The speed of sound in air is approximately 343 meters per second or 0.0343 centimeters per microsecond.

## Slide 49: Example 11 => Motion detection

## Slide 50: Example 11 => Motion detection

## Slide 51: Example 12 => Servo Motors

## Slide 52: Example 12 => Servo Motors

## Slide 53: Example 13 => DC Motors

## Slide 54: Example 13 => DC Motors

## Slide 55: Example 14 => H-Bridge

## Slide 56: Example 14 => H-Bridge

## Slide 57: Contact us