## Slide 1
Prepared by: Qossay Abu Rida
IEEE Robotics and Automation Society
Robot Maze Solver

## Slide 2: Agenda
Hardware
Micro-Controller
Wheels
H-Bridge
Sensors
Battery
Chassis
Software
What is required ?
Left Hand Rule
Right Hand Rule
Flood-Fill
Control

## Slide 3: Robot Hardware

## Slide 4
Micro-Controller
ESP32 is a low-cost, low-power system on a chip (SoC). It is widely used in IoT, embedded systems, and smart devices.
Key features include:
- Dual-core processor:
  Clock speeds up to 240 MHz.
- Connectivity:
Integrated Wi-Fi (802.11 b/g/n)
Bluetooth (BLE and Classic).
- Peripherals:
GPIO, ADC, DAC, UART, SPI, I2C, PWM.
- Rich development ecosystem:
Supported by Arduino IDE.
It’s ideal for applications like robotics.

## Slide 5
Brief About ESP32 (ESP32 CP2102 TYPE-C 38-Pin)

## Slide 6
ESP32 shield

## Slide 7
Wheels
Motor with Encoder:
Has a sensor to provide position, speed, and direction feedback for precise control.
Motor without Encoder:
Lacks feedback, offering simpler, cost-effective control but less accuracy.

## Slide 8
How encoder works:
Optical encoder. It uses an LED and a rotating disk. and light-receiving elements generate electrical signals. These signals represent the position, speed, and direction of the motor.

## Slide 9
H-Bridge (Motor Driver L298N)
L298N H-Bridge is a motor driver module that allows control of two DC motors. It supports forward/reverse rotation, speed control via PWM.

## Slide 10
How to connect:
Method 1:
Direction Control:
Two input pins (IN1, IN2) for each motor determine the motor's direction.
IN1= High , IN2 = Low → Motor rotates forward.
IN1= Low , IN2 = High → Motor rotates backward.
Speed Control:
Speed is adjusted using Pulse Width Modulation (PWM) applied to the Enable pin (EN).
Higher duty cycle → Faster speed.
Lower duty cycle → Slower speed
Method 2:
Direction and Speed Control:
Connect EN to 5 volt use jumper then
IN1 = PWM, IN2 = LOW → Forward speed controlled by IN1's PWM.
IN1 = LOW, IN2 = PWM → Reverse speed controlled by IN2's PWM.

## Slide 11
How H-Bridge works:

## Slide 12
Sensors (IR)
حاولوا ما تجيبوه لانه بشتغل على مزاجه وحساس للظروف الخارجية زيادة عن اللزوم

## Slide 13
Sensors (ultrasonic)
جيد بس مشكلته حجمه كبير شوي

## Slide 14
Sensors (Laser Range Finder Distance Sensor Time of Flight VL6180X)
خيار جيد وهسا بنشرح عنه بالتفصيل

## Slide 15
Sensors
It is a good idea to connect one sensor to a servo motor.
https://www.youtube.com/watch?v=Ro7T3q14uDY

## Slide 16
Battery (9 volt battery)
مش احسن خيار بس ممكن يريحكم اذا بلشتوا فيه ويوفر عليكم حرق قطع

## Slide 17
Battery (Lithium Ion Battery – 18650 Cell (5000mAh))

## Slide 18
Chassis

## Slide 19
EXAMPLE

## Slide 20: Robot Software

## Slide 21
What is required ?
The primary objective is for the robot to navigate through the maze and reach its center.
Once the robot has successfully explored the maze on its first attempt, its secondary goal is directly reaching the center on subsequent attempts without relying on its sensors to detect the maze's boundaries.

## Slide 22
How to write code ?
void loop (){
If (mazeValues [currentPosition.y][currentPosition.x]==0)
return ;
readSensors(); makeDecision();
moveMotor();
}

## Slide 23
Left Hand Rule Right Hand Rule

## Slide 24
Left or Right Hand Rule
In some cases, using the Left-Hand Rule or Right-Hand Rule alone may not lead to a solution when navigating a maze. To overcome this limitation and ensure the algorithm finds a path, we introduce a random choice between turning left or right at certain decision points

## Slide 25
Flood-Fill
Flood-Fill Algorithm is a critical component for dynamically updating the maze's distance matrix when an inconsistency occurs during navigation.
It ensures that all cells in the maze are correctly labeled with their distances to the target cell.
Flood-Fill similar with A* at some point:
1- Node Representation:
- Each cell in the maze is a node.
- A node is represented by its coordinates (𝑥,𝑦).
2- Costs:
- h(n): Heuristic estimating the distance from
the current cell to the goal cell.
- Use Manhattan distance for simplicity
3- Update:
- Updates distances globally and works well for dynamic updates
when new walls are detected

## Slide 26
Flood-Fill

## Slide 27
Flood-Fill

## Slide 28
Flood-Fill
1- The current cell must have a weight greater than at least one neighbor 2- Hence when all neighbors have values greater than the current cell
We need to edit the weights to achieve point 1
if (dp[current_cell.x][current_cell.y] - 1 != dp[min_cell.x][min_cell.y]) {
// edit weights
// add all neighbors to the qeueu
}

## Slide 29
Flood-Fill

## Slide 30
Flood-Fill

## Slide 31
Flood-Fill

## Slide 32
Flood-Fill

## Slide 33
Flood-Fill

## Slide 34
Flood-Fill

## Slide 35
Flood-Fill

## Slide 36
Flood-Fill

## Slide 37
Flood-Fill

## Slide 38: Motor Controller

## Slide 39
What is PID Control?
PID (Proportional-Integral-Derivative):
A feedback control algorithm.
Ensures precise and stable control of systems.
Purpose in Robotics:
Maintain a straight path by balancing motor speeds.

## Slide 40
Responsibilities of the PID control components (𝐾𝑝​, 𝐾𝑖​, 𝐾𝑑)
Proportional Gain (𝐾𝑝)
Responsibility: Reacts to the current error.
Effect: The larger the error, the stronger the correction.
Drives the system to reduce the error quickly. (may cause overshooting)
Integral Gain (𝐾𝑖)
Responsibility: Reacts to the accumulation of past errors.
Effect: remove drift in the system (removes steady-state error).
Eliminates steady-state errors over time.
Derivative Gain (𝐾𝑑)
Responsibility: Reacts to the rate of change of the error.
Effect: Predicts and dampens future errors based on the current trend.
Smoothens response and reduces overshooting.

## Slide 41
Method 1 - Using Encoders (Apply PID to Reach Reference Speed)
Purpose:
Ensure each motor reaches and maintains a target speed.
Steps:
Set Target Speed: Desired speed for each motor.
Measure Actual Speed: Use encoder data to calculate the current speed of each motor.
Calculate Speed Error
Apply PID Algorithm:
Compute the correction for each motor using PID.
Adjust motor speeds via PWM signals.
Adjust motor speeds dynamically using PID output: decrease the speed of the motor with a higher encoder count and increase the speed of the motor with a lower encoder count. This ensures synchronized rotations and straight-line movement.

## Slide 42
Method 2 - Using Encoders (Minimize Difference in Encoder Counts)
Purpose:
Ensure the robot moves straight by synchronizing motor rotations.
Steps:
Measure Encoder Counts: Track the number of rotations for each motor.
Calculate Difference in Counts
Calculate Speed Error
Apply PID Algorithm:
Adjust motor speeds to reduce the difference to zero.
Synchronize the motors dynamically.

## Slide 43
Method 3 - Using MPU6050 (Apply PID for Robot Orientation)
Purpose:
Maintain the robot’s position and heading.
Steps:
Set Target Orientation: Desired straight heading (yaw angle = 0°).
Measure Actual Orientation: Use MPU6050 to read the robot’s yaw angle.
Calculate Yaw Error
Apply PID Algorithm:
Adjust motor speeds to correct orientation.
Ensure the robot stays aligned with the target path.

## Slide 44
فإن وُفِّقتُ فمن فضل الله
The floor is open for your questions and inquiries now only